Micro Quadcopter components

Motors: hexTronik 5gram Brushless Outrunner 2000kv
http://hobbyking.com/hobbyking/store/__6312__hexTronik_5gram_Brushless_Outrunner_2000kv.html
Kv: 2000rpm/v
Weight: 5g
Voltage: 7.4v (2 cell Lipo)
Current: 2A
Suggested Propeller: 4x2.5
Thrust: 90g+
Shaft: 1.5mm

ESC: TURNIGY Plush 6A /.8bec/6g Speed Controller
http://hobbyking.com/hobbyking/store/__4318__TURNIGY_Plush_6A_8bec_6g_Speed_Controller.html

Model: Plush 6A
Continuous Current: 6A
Burst: 8A
BEC: Linear
BEC Output: 5v/.8A
Lipo Count: 2cell Guarenteed (3 cell capable but not warranted)
NiMH: 5-6
Programability: Programming card or Radio Controller
Weight: 6g
Size: 24x12x6mm

Battery: Rhino 460mAh 2s 7.4V 20C Lipoly Pack
http://hobbyking.com/hobbyking/store/__7303__Rhino_460mAh_2S_7_4v_20C_Lipoly_Pack.html?strSearch=rhino%20460

Capacity : 460mAh
Constant discharge: 20C
Burst rate: 30C (15sec)
Configuration : 2S 7.4v
Pack size: 52x30x8mm
Weight : 28.5g

Propellers: 4x2.5 (inches)
http://hobbyking.com/hobbyking/store/__41104__4x2_5R_Propellers_Green_R_H_Rotation_5Pcs_Bag_.html
http://hobbyking.com/hobbyking/store/__41103__4x2_5_Propellers_Green_5Pcs_Bag_.html

Autopilot: Paparazzi Lisa m 2.0
http://wiki.paparazziuav.org/wiki/Lisa/M_v20